## Slide 1
CHEESE APPLICATIONS

## Slide 2
FROMAGERIES BEL
LE Mans (France)
CHEESE BASE TEXTURIZING TANK

## Slide 3
PRODUCT :
CHEESE BASE
TEMPERATURE (25 TO 75°C)
VISCOSITY (2,000 to 6,000cP)
TANK :
VERTICAL
ATMOSPHERIC
ISOLATED
SINGLE JACKET
120°C CONICAL BOTTOM
CAPACITY : 600l.

## Slide 4
AGITATION :
VERTICAL, CENTRAL, WITHOUT GUIDING BEARING
ANCHOR TYPE + PITCHED BLADES + SCRAPERS
10RPM ROTATION SPEED (WITH TORQUE METER)
1.1KW MOTOR
SEE DWG A14451

## Slide 7
BOURSIN
Croisy Sur Eure (France)
CHEESE PASTE PREPARATION TANK

## Slide 8
PRODUCT :
CHEESE PASTE + GARLIC, SALT, PEPPER, HERBS
TEMPERATURE 60°C
VISCOSITY (8,000cP)
TANK :
VERTICAL
ATMOSPHERIC
ISOLATED
DOUBLE JACKET
CAPACITY : 450l.

## Slide 9
AGITATION 1 :
VERTICAL, CENTRAL, WITHOUT GUIDING BEARING
ANCHOR TYPE + SCRAPERS
15RPM ROTATION SPEED (WITH FREQUENCY INVERTER)
1.5KW MOTOR
AGITATION 2 :
VERTICAL, OFF-SET, WITHOUT GUIDING BEARING
PITCHED-BLADE TURBINE TYPE
35RPM ROTATION SPEED (WITH FREQUENCY INVERTER)
0.55KW MOTOR
SEE DWG A14228
ail, sel, poivre, persil, ciboulette

## Slide 10
ail, sel, poivre, persil, ciboulette

## Slide 11
ail, sel, poivre, persil, ciboulette

## Slide 12
EPI BRETAGNE
Yffignac (France)
MOLTEN CHEESE TANK

## Slide 13
PRODUCT :
MOLTEN CHEESE (Emmental, goat-cheese, etc) + CREAM
TEMPERATURE 40°C
VISCOSITY (6,000cP)
TANK :
VERTICAL
ULTRA-CLEAN (+0.49BAR, -1BAR)
ISOLATED
DOUBLE JACKET
CAPACITY : 2000l.

## Slide 14
AGITATION :
VERTICAL, CENTRAL, WITHOUT GUIDING BEARING
ANCHOR TYPE + PITCHED-BLADES & SCRAPERS
25RPM ROTATION SPEED (WITH FREQUENCY INVERTER)
4KW MOTOR
SEE DWG A12872
ail, sel, poivre, persil, ciboulette

## Slide 15
ail, sel, poivre, persil, ciboulette

## Slide 16
ail, sel, poivre, persil, ciboulette

## Slide 17
NOVANDIE
Auneau (France)
WHITE CHEESE MIXING TANK

## Slide 18
PRODUCT :
WHITE CHEESE « Fromage Blanc » + EGGS, STARCH, FLAVOURS
TEMPERATURE 4°C
VISCOSITY (3,000cP)
TANK :
VERTICAL
ULTRA-CLEAN (+0.49BAR, -1BAR)
NON ISOLATED
SINGLE JACKET
CAPACITY : 800l.

## Slide 19
CONTRA-ROTATION AGITATION 1 :
VERTICAL, CENTRAL, WITHOUT GUIDING BEARING
ANCHOR TYPE + SCRAPERS
30RPM ROTATION SPEED (WITH FREQUENCY INVERTER)
5.5KW MOTOR
CONTRA-ROTATION AGITATION 2 :
VERTICAL, CENTRAL, WITHOUT GUIDING BEARING
PITCHED-BLADE TURBINE TYPE
92RPM ROTATION SPEED (WITH FREQUENCY INVERTER)
4KW MOTOR
SEE PDF D18195
ail, sel, poivre, persil, ciboulette

## Slide 20
ail, sel, poivre, persil, ciboulette

## Slide 21
ail, sel, poivre, persil, ciboulette